## Slide 1: Multi-Agent Yield Analysis For Circuit Design
Authors: Haiyan Qin, Jing Kou, Liang Zhang, Wang Kang, Wei W. Xing
School of Integrated Circuit Science and Engineering, Beihang University, Beijing, China;
School of Mathematical and Physical Sciences, University of Sheffield, Sheffield, United Kingdom
Notes: Good morning, everyone. I'm here to present our research on "Multi-Agent Yield Analysis For Circuit Design," which introduces YieldAgent - a novel LLM-powered framework that revolutionizes semiconductor yield estimation.
This is collaborative work between Beihang University and the University of Sheffield. Our research addresses critical challenges in modern semiconductor manufacturing by leveraging artificial intelligence to optimize yield estimation processes.

## Slide 2: Outline
Introduction and Background
YieldAgent Methodology
  System overview and design principles
  Multi-agent architecture
  Knowledge integration and method selection
  Dynamic hyperparameter optimization
  Statistical convergence analysis
  Integrated workflow
Experiment Results
  Budget-aware capability evaluation
  Precision-aware capability evaluation
  Topology-aware capability evaluation
Conclusion
Notes: Today's presentation is structured into four main sections. First, I'll provide an introduction and background on the challenges facing yield analysis in modern semiconductor manufacturing. Second, I'll present our YieldAgent methodology, including the system overview, multi-agent architecture, knowledge integration mechanisms, and our integrated workflow. Third, I'll share our comprehensive experiment results, demonstrating YieldAgent's capabilities across budget-aware, precision-aware, and topology-aware scenarios. Finally, I'll conclude with our key contributions and future directions.

## Slide 3: Introduction and Background
Notes: Let me begin by explaining why yield analysis is such a critical challenge in today's semiconductor industry.

## Slide 4: Challenges in Yield Analysis
As semiconductor technology advances, yield analysis faces increasing complexity and demands
Growing Circuit Complexity
Modern ICs integrate billions of transistors,
exponentially increasing the dimensionality of
analysis and overwhelming traditional methods
Process Variation Sensitivity
Shrinking feature sizes increase sensitivity to
manufacturing variations in oxide thickness,
threshold voltage, and carrier mobility
Computational Ineﬃciency
Traditional Monte Carlo methods are
prohibitively ineﬃcient for rare failure events,
requiring an impractical number of simulations
Topology Adaptability
Analysis methods often require expert
knowledge to adapt to diﬀerent circuit
topologies, limiting generalizability across designs
These challenges create the "impossible triangle" of yield analysis: simultaneously achieving high accuracy,
computational eﬃciency, and broad topology adaptability
Notes: As semiconductor technology advances toward smaller process nodes, yield analysis faces unprecedented complexity and demands. We've identified four fundamental challenges that create what we call the "impossible triangle" of yield analysis.
The first challenge is growing circuit complexity. Modern integrated circuits contain billions of transistors, which exponentially increases the dimensionality of analysis and overwhelms traditional methods that were designed for simpler circuits. The second challenge involves process variation sensitivity, where shrinking feature sizes dramatically increase sensitivity to manufacturing variations in parameters like oxide thickness, threshold voltage, and carrier mobility. These variations can cause significant performance fluctuations that are difficult to predict and analyze.
The third challenge is computational inefficiency. Traditional Monte Carlo methods become prohibitively inefficient for rare failure events, requiring an impractical number of simulations that can take days or weeks to complete, making them unsuitable for modern design cycles. The fourth challenge is topology adaptability, where existing analysis methods often require expert knowledge to adapt to different circuit topologies, severely limiting their generalizability across diverse designs and technology nodes.
These challenges create the fundamental trade-off problem of simultaneously achieving high computational efficiency, estimation accuracy, and broad topology adaptability.

## Slide 5: Limitations of Current Methods
Monte Carlo
Simulation
Extremely ineﬃcient for rare
events (low failure probabilities)
Requires excessive number of
simulations for accuracy
Computationally prohibitive for
complex circuits
Poor scaling with increasing circuit
dimensions
Importance
Sampling
Requires expert knowledge to
deﬁne optimal sampling
distribution
Highly dependent on circuit
topology
Poor generalization across diﬀerent
designs
Enhanced versions (MNIS, GIS,
FSIS, AIS, HSCS, ACS) still face
topology adaptability challenges
Surrogate
Models
Require substantial training data
Limited accuracy for complex or
high-dimensional circuits
Need extensive retraining for new
designs
Common approaches (LRTA, BYA,
ASDK) lack adaptability across
technology nodes
Struggle with rare failure events
prediction
Notes: Let me elaborate on the specific limitations of current approaches:
Monte Carlo Simulation remains the gold standard for accuracy but is extremely inefficient for rare events with low failure probabilities. It requires excessive simulations and scales poorly with increasing circuit dimensions.
Importance Sampling methods like MNIS, GIS, and HSCS offer better efficiency but require substantial expert knowledge to define optimal sampling distributions. They're highly dependent on circuit topology and show poor generalization across different designs.
Surrogate Models including approaches like LRTA, BYA, and ASDK require extensive training data and show limited accuracy for complex, high-dimensional circuits. They need constant retraining for new designs and struggle with rare failure event prediction.
These limitations highlight the urgent need for a more intelligent, adaptive approach to yield estimation.

## Slide 6: The Impossible Triangle
The Fundamental Trade-off:
Estimation Accuracy:
Essential for reliable yield prediction
Traditional high-accuracy methods require massive simulations
Critical for high-reliability applications like SRAM
Computational Efficiency:
Growing concern as circuits become more complex
Each simulation may require hours of computation
Limited resources in industrial design flows
Topology Adaptability:
Different circuits require different estimation strategies
Technology node transitions introduce new failure mechanisms
One-size-fits-all approaches typically fail
YieldAgent's Breakthrough:
Uniquely balances all three dimensions through multi-agent framework
Achieves 5.84× to 20× reduction in simulations while maintaining or improving accuracy
Demonstrated across both 12nm and 40nm technology nodes
Notes: This slide illustrates the fundamental challenge we're addressing. Traditional methods can typically excel in one or two dimensions but fail to balance all three requirements simultaneously.
Monte Carlo provides high accuracy but low efficiency. Importance Sampling offers better efficiency but limited adaptability. Surrogate Models improve efficiency but depend heavily on training data. Advanced IS methods achieve good accuracy and efficiency but remain topology-specific.
YieldAgent's breakthrough lies in its ability to uniquely balance all three dimensions through our multi-agent framework. We achieve 5.84× to 20× reduction in simulations while maintaining or improving accuracy, demonstrated across both 12nm and 40nm technology nodes.
This represents a paradigm shift from fixed, single-method approaches to dynamic, intelligent strategy integration.

## Slide 7: YieldAgent A novel LLM-powered framework for yield estimation
Notes: Now let me introduce YieldAgent - our novel LLM-powered framework for yield estimation that transforms how we approach this critical challenge.

## Slide 8: System overview and design principles
Advantages:
Dynamic integration of methods, adaptability, efficiency
Three Key Capabilities
Budget-aware Resource Optimization
Intelligently allocates computational resources based on analysis
requirements and constraints, maximizing eﬀectiveness within budget limitations.
Precision-guided Estimation
Dynamically adjusts estimation strategies to achieve required precision levels,
employing advanced statistical techniques for convergence assessment.
Topology-aware Method Selection
Adapts analysis approaches based on circuit characteristics across diﬀerent
technology nodes, ensuring optimal method selection for each speciﬁc design.
Notes: YieldAgent is built on three key capabilities that distinguish it from existing approaches and enable it to break through the impossible triangle. The first capability is budget-aware resource optimization, where the system intelligently allocates computational resources based on analysis requirements and constraints, maximizing effectiveness within budget limitations. This ensures optimal use of available computing power by dynamically adjusting the allocation of simulations across different methods based on their performance characteristics and the remaining computational budget.
The second capability is precision-guided estimation, where YieldAgent dynamically adjusts estimation strategies to achieve required precision levels by employing advanced statistical techniques for convergence assessment. This allows for flexible quality control based on specific needs, automatically switching between faster approximate methods and more precise techniques as convergence requirements dictate.
The third capability is topology-aware method selection, where the framework adapts analysis approaches based on circuit characteristics across different technology nodes, ensuring optimal method selection for each specific design. The system learns from historical performance data and real-time analysis to select the most appropriate combination of methods for each unique circuit topology and technology node combination.
The key advantage of this approach is the dynamic integration of methods, providing adaptability and efficiency that traditional single-method approaches cannot match.

## Slide 9: Multi-agent architecture
Strategic Layer:
Strategy Agent: Sets goals and analyzes circuit characteristics
Coordination Layer:
Coordination Agent: Manages tasks and method selection
Database Agent: Retrieves historical performance data
Execution Layer:
Code Gen. Agent: Implements selected methods
Execution Agent: Manages simulation resources
Analysis Agent: Evaluates convergence and results
Optimizer Agent: Tunes hyperparameters dynamically
Notes: Our multi-agent architecture implements a hierarchical three-layer design that separates strategic planning from tactical execution, enabling specialized expertise at each level while maintaining coordinated system-wide behavior. The Strategic Layer contains the Strategy Agent, which operates at the highest level to set goals and analyze circuit characteristics for developing high-level estimation strategies. This agent leverages LLM reasoning capabilities to understand the overall requirements and constraints of each yield analysis task.
The Coordination Layer features two specialized agents working in harmony. The Coordination Agent manages tasks and method selection, serving as the central coordinator that translates high-level strategies into specific execution plans. The Database Agent handles knowledge integration and retrieval of historical performance data, maintaining the institutional memory of what methods work best under different conditions.
The Execution Layer comprises four specialized agents that handle the detailed implementation work. The Code Generation Agent creates tailored implementations of selected methods, producing executable code optimized for the specific circuit and analysis requirements. The Execution Agent manages simulation resources and workflow execution, ensuring efficient utilization of computational resources. The Analysis Agent evaluates convergence and results, providing real-time feedback on estimation quality and convergence status. Finally, the Optimizer Agent tunes hyperparameters dynamically using advanced optimization techniques to ensure peak performance throughout the analysis process.
This separation of concerns enables each agent to specialize in its domain while maintaining systematic coordination through LLM-based reasoning.

## Slide 10: Knowledge Integration Mechanism
Retrieval-Augmented Generation
(RAG)
Enhances LLM capabilities with domain-speciﬁc
knowledge retrieval
Integrates semiconductor yield analysis expertise and
methodologies
Enables context-aware decision making for complex
circuit scenarios
Provides accurate responses based on validated
knowledge
Database-Driven Method
Selection
Curated database of validated yield analysis
methodologies
Performance proﬁles across diﬀerent technology nodes
Dynamic method selection based on circuit
characteristics
Supports MNIS, HSCS, AOSM, and ACS
methodologies
Domain Knowledge
RAG Processing
Method Selection
Circuit Analysis
Notes: YieldAgent leverages two key mechanisms for intelligent decision-making:
Retrieval-Augmented Generation (RAG) enhances LLM capabilities with domain-specific knowledge retrieval. This integrates semiconductor yield analysis expertise and methodologies, enabling context-aware decision making for complex circuit scenarios while providing accurate responses based on validated knowledge.
Database-Driven Method Selection maintains a curated database of validated yield analysis methodologies including MNIS, HSCS, AOSM, and ACS. This provides performance profiles across different technology nodes and supports dynamic method selection based on circuit characteristics.
The workflow progresses from Domain Knowledge through RAG Processing and Method Selection to final Circuit Analysis, ensuring that every decision is informed by both historical data and real-time performance metrics.

## Slide 11: Knowledge integration and method selection
Retrieval-Augmented Generation (RAG) for domain knowledge
Database of validated methodologies (MNIS, HSCS, AOSM, ACS)
Performance profiles across technology nodes
Dynamic strategy adjustment based on circuit characteristics
Notes: Our knowledge integration system demonstrates its effectiveness through comprehensive performance analysis across different technology nodes. The system incorporates Retrieval-Augmented Generation for domain knowledge integration while maintaining a carefully curated database of validated methodologies including MNIS, HSCS, AOSM, and ACS with detailed performance profiles across technology nodes.
The graphs show experimental results on 40nm and 12nm nodes, demonstrating how different methods perform across varying numbers of simulations. You can see the convergence behavior and relative performance of each approach, which informs our dynamic strategy adjustment based on circuit characteristics.
This data-driven approach enables YieldAgent to make intelligent decisions about method selection and resource allocation in real-time.

## Slide 12: Dynamic Hyperparameter Optimization
Tree-structured Parzen Estimator (TPE) approach
Empirical analysis showing performance degradation across nodes without adjustment
Modeling relationship between hyperparameters and estimation performance
Selecting hyperparameters by maximizing expected improvement
Statistical Convergence Analysis
Sliding window statistical approach for stability assessment
Relative Variation for convergence detection
Advantages: Robustness to fluctuations, adaptive sensitivity, efficiency
Notes: A critical innovation in YieldAgent is our dynamic hyperparameter optimization using Tree-structured Parzen Estimators (TPE).
Our empirical analysis shows significant performance degradation when methods optimized for one technology node are applied to another without adjustment. The graphs clearly show gaps between 40nm-optimized configurations and actual performance on 12nm nodes.
YieldAgent addresses this through TPE that models the relationship between hyperparameters and estimation performance, selecting hyperparameters by maximizing expected improvement. This ensures optimal performance across different technology nodes and circuit characteristics.
Our Statistical Convergence Analysis uses a sliding window approach with Relative Variation for convergence detection, providing robustness to fluctuations, adaptive sensitivity, and computational efficiency.

## Slide 13: Statistical Convergence Analysis
Sliding Window Approach
YieldAgent employs a sliding window statistical
method to assess stability and detect convergence
in yield estimation results.
Monitors estimation stability across consecutive simulation batches
Window size k = 5 for optimal balance between sensitivity and
noise ﬁltering
Relative Variation used as convergence metric
Key Advantages
Robustness
Resilient to temporary
ﬂuctuations in estimation
Adaptive Sensitivity
Adjusts based on estimation
magnitude
Eﬃciency
Prevents unnecessary
simulations
Balance
Optimizes accuracy vs.
computation trade-oﬀ
Sliding Window Visualization
Relative Variation = σ/μ<ε
σ: Standard deviation of estimates in window
μ: Mean of estimates in window
ε: Convergence threshold (user-deﬁned)
Notes: Our sliding window approach provides robust convergence assessment specifically designed for dynamic, multi-model scenarios that characterize modern yield analysis challenges. The system monitors estimation stability across consecutive simulation batches using a carefully chosen window size of k=5, which provides the optimal balance between sensitivity to genuine convergence and noise filtering to avoid premature termination due to temporary fluctuations.
The approach offers several key advantages that make it particularly suitable for our multi-agent framework. It provides robustness by being resilient to temporary fluctuations in estimation that can occur when switching between methods or adjusting parameters. It offers adaptive sensitivity that automatically adjusts based on the magnitude of the estimates, ensuring appropriate convergence criteria for both high and low probability events. The method maintains computational efficiency by preventing unnecessary simulations once true convergence is achieved, while still maintaining the accuracy requirements specified by the user. Finally, it optimizes the fundamental trade-off between accuracy and computation time, allowing users to specify their requirements and letting the system find the most efficient path to meet them.
The convergence criterion uses Relative Variation calculated as the ratio of standard deviation to mean within the sliding window, compared against a user-defined threshold. This relative approach ensures that convergence criteria scale appropriately with the magnitude of the failure probabilities being estimated.

## Slide 14: Integrated Workflow
1. Input Phase
• Circuit parameters and topology specifications
• Technology node information
• Precision requirements and computational budget
2. Planning Phase
• Strategy Agent analyzes input and circuit characteristics
• Database Agent retrieves relevant historical performance data
• Coordination Agent selects initial methods and allocates resources
3. Execution Phase
• Code Generation Agent creates tailored implementation
• Execution Agent runs simulations with monitored convergence
• Optimizer Agent tunes hyperparameters through TPE
4. Analysis & Feedback
• Convergence assessment using sliding window approach
• Real-time performance evaluation and method adjustment
• Final results compilation and reporting
Example: 6T-SRAM at 12nm
Input: 12nm SRAM, ε=0.05, max 50K simulations
Planning: Selected ACS+AOSM combination based on topology
Execution: Dynamic TPE optimization reduced simulation needs by 9.03×
Result: 3.4% relative error using only 23,000 simulations
Notes: Let me walk you through YieldAgent's integrated workflow using a practical example that demonstrates how all the components work together in a real analysis scenario. We'll examine the analysis of a 6T-SRAM circuit at 12nm technology node, which represents a challenging but common industrial scenario.
The workflow begins with the Input Phase, where users specify circuit parameters and topology specifications, technology node information, precision requirements, and computational budget constraints. This information forms the foundation for all subsequent optimization decisions. The Planning Phase follows, where the Strategy Agent analyzes the input and circuit characteristics to understand the fundamental challenges and requirements. Simultaneously, the Database Agent retrieves relevant historical performance data from similar analysis scenarios, while the Coordination Agent synthesizes this information to select initial methods and allocate computational resources strategically.
The Execution Phase represents the core of the analysis process. The Code Generation Agent creates tailored implementations of the selected methods, optimizing the code for the specific circuit characteristics and computational environment. The Execution Agent then manages the simulation runs while maintaining monitored convergence tracking, ensuring that computational resources are used efficiently. Throughout this process, the Optimizer Agent continuously tunes hyperparameters using our Tree-structured Parzen Estimator approach, adapting to real-time performance feedback.
The final Analysis and Feedback Phase employs our sliding window convergence assessment approach to determine when sufficient accuracy has been achieved. The system provides real-time performance evaluation and method adjustment capabilities, allowing for dynamic strategy modification if initial approaches prove suboptimal. Finally, comprehensive results compilation and reporting provide detailed insights into both the yield estimates and the analysis process itself.
In our specific example with 12nm SRAM analysis using a convergence factor of 0.05 and maximum 50,000 simulations, the system intelligently selected an ACS+AOSM combination based on historical performance data and circuit topology analysis. Through dynamic TPE optimization, the system reduced simulation requirements by a factor of 9.03, ultimately achieving 3.4% relative error using only 23,000 simulations, well within the specified computational budget.

## Slide 15: Experiment
Notes: Now let me present our comprehensive experimental validation.

## Slide 16: Experimental Setup
Implementation Details
Framework: Microsoft AutoGen with GPT-4o-mini
Computing: AMD EPYC 7601 CPU, 62GB RAM
Simulation: HSPICE
Convergence: Sliding window size k = 5
Test Vehicle
Circuit: 6T-SRAM bit cell
Technology nodes: TSMC 12nm and SMIC 40nm
Process variations:
Oxide thickness
Threshold voltage
Carrier mobility
Performance metrics: Read/write delay
Notes: Our implementation uses Microsoft AutoGen with GPT-4o-mini, running on AMD EPYC 7601 CPU with 62GB RAM, using HSPICE for simulation with a sliding window size of k=5 for convergence.
We use a 6T-SRAM bit cell as our test vehicle across TSMC 12nm and SMIC 40nm technology nodes. Process variations include oxide thickness, threshold voltage, and carrier mobility, with performance metrics focused on read/write delay.
This setup provides a rigorous testbed for evaluating YieldAgent's capabilities across different technology nodes and operating conditions.

## Slide 17: Budget-Aware Capability Results
Comparison across three budget levels:
Low (3,000), Medium (6,000), High (10,000)
Key Insights:
YieldAgent consistently outperforms single-method approaches across all budget levels
Dynamic method combination adapts to available resources
Even at low budget (3,000 simulations), YieldAgent achieves 4.1% error vs. best alternative at 8.6%
Method selection pattern: MNIS+ACS+AOSM for low budget, MNIS+AOSM for higher budgets
Relative Error Comparison
Notes: Our budget-aware evaluation provides comprehensive assessment of YieldAgent's resource optimization capabilities by comparing performance across three distinct computational budget scenarios: Low budget with 3,000 simulations, Medium budget with 6,000 simulations, and High budget with 10,000 simulations. This evaluation positions YieldAgent against both traditional Monte Carlo simulation and four state-of-the-art methods: MNIS, AOSM, ACS, and HSCS, using a reference failure rate of 6.91 × 10^-4 established through extensive Monte Carlo simulation with 110,000 samples.
The results demonstrate YieldAgent's consistent superiority across all budget levels through intelligent method integration. Under the stringent Low budget constraint, YieldAgent achieves remarkable 4.1% relative error using only 2,890 simulations through dynamic combination of MNIS, AOSM, and ACS methods. This performance significantly surpasses the best single-method approach, which was ACS achieving 8.6% error with 2,980 simulations, demonstrating the power of intelligent method combination even under severe resource constraints.
In the Medium budget scenario, YieldAgent showcases superior method integration capabilities by strategically combining MNIS with iterative AOSM refinements. This approach achieves 2.96% relative error using 5,550 simulations, while traditional fixed methods exhibit errors ranging from 3.4% to 6.7%. The High budget evaluation further demonstrates YieldAgent's strategic optimization capabilities, where the combination of MNIS and AOSM iterations yields 1.8% relative error with 9,200 simulations, compared to AOSM's standalone performance of 3.6% error using 9,950 simulations. These results clearly show that YieldAgent's intelligent resource allocation and method combination strategies consistently outperform traditional approaches across the entire range of computational budgets.

## Slide 18: Precision-Aware Capability Results
Performance Highlights:
For ε=0.1: 2.7% error with 5,550 #Sim
(HSCS needs 16,100 simulations for similar accuracy)
For ε=0.05: 1.0% error with 8,760 #Sim (2.37× reduction from HSCS)
For ε=0.01: 0.4% error with 15,600 #Sim
(Superior accuracy with 1.5× fewer simulations than MNIS)
Method Selection Evolution:
As precision requirements increase, YieldAgent shifts from ACS+MNIS (ε=0.1) to ACS+HSCS (ε=0.01)
Notes: Our precision-aware evaluation assesses YieldAgent's ability to meet varying accuracy requirements defined by convergence factors of 0.1, 0.05, and 0.01, representing increasingly stringent precision demands typical of different industrial applications. The evaluation employs relative error and simulation count as primary metrics, with convergence determined when the relative variation in yield estimates falls below the specified threshold across our sliding window analysis approach.
The performance results demonstrate YieldAgent's exceptional adaptability to precision requirements across all tested scenarios. For the most relaxed precision requirement of ε=0.1, YieldAgent achieves 2.7% error with only 5,550 simulations, while HSCS requires 16,100 simulations to achieve similar 2.6% accuracy, representing a nearly 3-fold improvement in computational efficiency. Under the moderate precision requirement of ε=0.05, YieldAgent maintains superior performance with 1.0% error using 8,760 simulations, achieving a 2.37-fold reduction compared to HSCS which requires 20,800 simulations for 2.5% accuracy.
Most impressively, under the strictest precision requirement of ε=0.01, YieldAgent delivers 0.4% error with 15,600 simulations, demonstrating superior accuracy with 1.5 times fewer simulations than MNIS, which achieves 0.9% error with 23,300 simulations. This performance showcases YieldAgent's ability to maintain efficiency even under demanding accuracy requirements.
The method selection evolution reveals YieldAgent's intelligent adaptation strategy. As precision requirements increase from ε=0.1 to ε=0.01, the system intelligently shifts from ACS+MNIS combinations for moderate precision to ACS+HSCS combinations for highest precision demands. This demonstrates the system's ability to automatically select the most appropriate method combinations based on user-specified accuracy requirements rather than relying on fixed strategies.

## Slide 19: Topology-Aware Capability Results
Key Findings
Adaptation across TSMC 12nm
and SMIC 40nm technology nodes
Dynamic method selection based
on technology:
ACS-MNIS/HSCS for 40nm
ACS-AOSM for 12nm
Simulation reduction factors:
5.84×-20× across conﬁgurations
Maintained estimation accuracy
with relative errors as low as 0.4%
Notes: Our topology-aware evaluation demonstrates YieldAgent's remarkable adaptation capabilities across TSMC 12nm and SMIC 40nm technology nodes, which represent significantly different manufacturing processes with distinct variation characteristics and failure mechanisms. The 12nm node exhibits tighter threshold voltage variations and more complex failure region geometries compared to the 40nm node, presenting fundamentally different estimation challenges that require adapted analytical approaches.
The key findings reveal YieldAgent's sophisticated adaptation across technology nodes through dynamic method selection based on technology-specific characteristics. For the 40nm technology node, the system intelligently selects ACS-MNIS and ACS-HSCS combinations that are well-suited to the broader variation spreads and simpler failure region geometries characteristic of this older process technology. Conversely, for the 12nm node with its tighter variations and more complex failure mechanisms, YieldAgent adapts by employing ACS-AOSM combinations that are better equipped to handle the intricate failure region boundaries and higher-dimensional correlation structures.
The computational efficiency results are remarkable, with simulation reduction factors ranging from 5.84 to 20 times across different configurations while maintaining estimation accuracy with relative errors as low as 0.4%. These results demonstrate that YieldAgent not only adapts its methodology to different technologies but does so while achieving substantial computational savings. The performance differences between nodes clearly illustrate YieldAgent's topology-aware capabilities, where the system automatically recognizes the distinct characteristics of each technology and selects the most appropriate method combinations accordingly.
This adaptive behavior represents a significant advancement over traditional approaches that typically require manual expert intervention to optimize methods for different technology nodes, making YieldAgent particularly valuable for organizations working across multiple process technologies or transitioning between technology generations.

## Slide 20: Key Contributions
1. LLM-Powered Multi-Agent Architecture
Three-layer design separating strategy from execution
RAG for domain knowledge integration
Dynamic agent coordination for adaptive decisions
2. Dynamic Knowledge Integration
Historical data + real-time performance analysis
TPE for efficient hyperparameter optimization
Sliding window approach for robust convergence
3. Cross-Technology Validation
Proven across 12nm and 40nm nodes
Up to 2.9× reduction in computational cost
Maintaining or improving estimation accuracy
Industrial Impact:
Significant time and cost savings
Better yield predictions for manufacturing
Adaptability to technology scaling challenges
Notes: Our research makes three fundamental contributions that collectively break through the impossible triangle of yield estimation, addressing the long-standing challenge of simultaneously achieving accuracy, efficiency, and adaptability. The first contribution is our LLM-Powered Multi-Agent Architecture, which introduces a novel three-layer design that strategically separates high-level planning from tactical execution. This architecture incorporates Retrieval-Augmented Generation for seamless domain knowledge integration and enables dynamic agent coordination for truly adaptive decision-making processes that can respond to changing conditions in real-time.
The second contribution involves Dynamic Knowledge Integration, where we combine historical performance data with real-time analysis to create a continuously learning system. Our implementation employs Tree-structured Parzen Estimators for efficient hyperparameter optimization that adapts to different technology nodes and circuit characteristics. Additionally, our sliding window approach provides robust convergence assessment that balances accuracy requirements with computational efficiency, ensuring reliable results across diverse analysis scenarios.
Our third contribution is comprehensive Cross-Technology Validation, where we have proven YieldAgent's effectiveness across both 12nm and 40nm technology nodes, achieving up to 2.9 times reduction in computational cost while maintaining or improving estimation accuracy compared to existing state-of-the-art methods. This validation demonstrates the practical utility and broad applicability of our approach across different manufacturing technologies.
The industrial impact of this work translates directly to significant time and cost savings for semiconductor manufacturers, enabling better yield predictions that can inform manufacturing decisions and design optimizations. The adaptability to technology scaling challenges makes YieldAgent particularly valuable as the industry continues to push toward smaller process nodes with increasingly complex variation characteristics. The diagram illustrates how YieldAgent uniquely positions itself at the center of the impossible triangle, successfully balancing all three critical requirements that have traditionally forced trade-offs in yield estimation approaches.

## Slide 21: Key Contributions
LLM-Powered Multi-
Agent Architecture
Innovative framework with
specialized intelligent agents
Addresses the "impossible triangle"
challenge in yield analysis
Balances accuracy, eﬃciency, and
adaptability
Dynamic Knowledge
Integration
Retrieval-Augmented Generation
(RAG) for domain knowledge
Database of validated
methodologies (MNIS, HSCS, AOSM,
ACS)
Tree-structured Parzen Estimator for
hyperparameter optimization
Cross-Technology
Validation
Validated across TSMC 12nm and
SMIC 40nm nodes
5.84× to 20× reduction in required
simulations
Maintains or improves estimation
accuracy across technologies
YieldAgent establishes a new paradigm for semiconductor yield estimation, achieving a 2.9×
reduction in computational overhead while maintaining accuracy
Notes: YieldAgent establishes a new paradigm for semiconductor yield estimation, achieving a 2.9× reduction in computational overhead while maintaining accuracy.
Our three key innovations work synergistically to create capabilities that exceed the sum of their individual contributions. The LLM-Powered Multi-Agent Architecture provides an innovative framework with specialized intelligent agents that directly addresses the impossible triangle challenge by balancing accuracy, efficiency, and adaptability through coordinated decision-making processes that leverage the reasoning capabilities of large language models.
Dynamic Knowledge Integration represents our second major innovation, utilizing Retrieval-Augmented Generation to incorporate domain-specific knowledge while maintaining a comprehensive database of validated methodologies including MNIS, HSCS, AOSM, and ACS. The Tree-structured Parzen Estimator approach for hyperparameter optimization ensures that the system continuously adapts to achieve optimal performance across different scenarios and technology nodes.
Cross-Technology Validation, our third innovation, has been rigorously validated across TSMC 12nm and SMIC 40nm nodes, achieving between 5.84 and 20 times reduction in required simulations while maintaining or improving estimation accuracy across technologies. This comprehensive validation demonstrates not just the theoretical soundness of our approach but its practical utility in real-world semiconductor manufacturing scenarios.
Together, these innovations create a robust, intelligent framework that transforms how yield estimation is approached in modern semiconductor manufacturing, providing a foundation for continued advancement as technology nodes become increasingly challenging to analyze.

## Slide 22: Conclusions & Future Work
Notes: Now let me conclude with our key findings and future directions.

## Slide 23: Conclusions & Future Work
Conclusions
Future Directions
YieldAgent establishes a new paradigm for
semiconductor yield estimation
Successfully balances computational eﬃciency
and precision across circuit topologies
Achieves 5.84× to 20× reduction in required
simulations while maintaining or improving
accuracy
Multi-agent architecture provides dynamic
knowledge integration and optimization
capabilities
Demonstrates eﬀective cross-technology
validation across multiple circuit types
EDA Integration: Incorporate YieldAgent into
broader electronic design automation workﬂows
Circuit Topology Expansion: Extend
capabilities to support more diverse and complex
circuit architectures
Enhanced Reasoning: Improve agent reasoning
capabilities for more nuanced analysis and
recommendations
Industry Collaboration: Partner with
semiconductor manufacturers to validate and
reﬁne methodologies
Academic Research: Explore novel AI
techniques to further improve multi-agent
coordination
Notes: YieldAgent establishes a new paradigm for semiconductor yield estimation by successfully balancing computational efficiency and precision across circuit topologies. We achieve 5.84× to 20× reduction in required simulations while maintaining or improving accuracy. Our multi-agent architecture provides dynamic knowledge integration and optimization capabilities, with effective cross-technology validation across multiple circuit types.
Looking toward the future, we envision several exciting directions for expanding this work. EDA Integration represents a natural next step, where we plan to incorporate YieldAgent into broader electronic design automation workflows, enabling seamless integration with existing design tools and methodologies used throughout the semiconductor industry. Circuit Topology Expansion will extend our capabilities to support more diverse and complex circuit architectures beyond SRAM, including analog circuits, processors, and emerging device technologies that present unique yield analysis challenges.
Enhanced Reasoning capabilities represent another promising direction, where we aim to improve agent reasoning capabilities for more nuanced analysis and recommendations that can provide deeper insights into yield optimization strategies. Industry Collaboration offers opportunities to partner with semiconductor manufacturers to validate and refine our methodologies in real production environments, ensuring that our academic innovations translate effectively to practical manufacturing benefits.
Finally, Academic Research directions include exploring novel AI techniques to further improve multi-agent coordination, investigating applications to other areas of electronic design automation, and developing new theoretical frameworks for intelligent optimization in complex engineering scenarios. These future directions ensure that YieldAgent serves as a foundation for continued innovation in intelligent manufacturing and design optimization.

## Slide 24: Research Team Introduction
Prof. Wang Kang
School of Integrated Circuit Science and Engineering
Beihang University, Beijing, China
Leading researcher in post-Moore era computing
technologies with focus on next-generation AI
hardware and design methodologies.
Research Achievements
Over 200 SCI journal publications (including Nature
Electronics)
4 book chapters
Over 40 invention patents (15 granted, 12
commercialized)
Multiple national research projects including National
Key R&D Program of China
Research Focus Areas
In-Memory Computing AI Chips
Developing novel chip architectures that integrate memory
and processing units to overcome the von Neumann
bottleneck, improving energy eﬃciency and performance
for AI applications.
EDA Toolchains
Building sophisticated toolchains that support the entire
design ﬂow of AI chips, from high-level algorithmic
speciﬁcation to physical layout, including design space
exploration and co-optimization.
Algorithm Acceleration
Investigating and implementing hardware-aware AI
algorithms and specialized accelerator designs to boost
performance and eﬃciency of AI tasks, particularly in
resource-constrained environments.
Notes: I'd like to acknowledge our research team led by Prof. Wang Kang from the School of Integrated Circuit Science and Engineering at Beihang University. Prof. Wang is a leading researcher in post-Moore era computing technologies with over 200 SCI journal publications and extensive work in in-memory computing AI chips, EDA toolchains, and algorithm acceleration.
This collaborative effort represents the intersection of advanced AI techniques with critical semiconductor manufacturing challenges.

## Slide 25: Acknowledgments & Contact
This work was supported by Key R\&D Program of Shandong Province, China，2022CXGC020208, Beijing Municipal Natural Science Foundation (Z230004), the Beijing Natural Science Foundation (L223004), Natural Science Foundation of China (62274008) and Beijing MSTC Program (Z231100007423019
Notes: This work was supported by multiple funding sources including the Key R&D Program of Shandong Province, Beijing Municipal Natural Science Foundation, Beijing Natural Science Foundation, Natural Science Foundation of China, and Beijing MSTC Program.

## Slide 26
Notes: Thank you for your attention. YieldAgent represents a significant step forward in intelligent yield estimation, addressing real industrial challenges while opening new research directions. The combination of multi-agent systems, LLM reasoning, and domain-specific knowledge creates a powerful framework that we believe will transform how the semiconductor industry approaches yield analysis.
I welcome any questions you may have about our methodology, experimental results, or potential applications of this work.